|  | SPICe science briefing December 2003 03/03 |
| --- | --- |
| toxins in tobacco smoke: effectiveness of air filtration and ventilation systems |  |
| introduction This briefing provides information on the toxins present in tobacco smoke and considers the effectiveness of air filtration and ventilation systems in extracting these toxins from the air. No ventilation system can effectively remove all toxin-bearing tobacco smoke from a public house or restaurant. |  |

## background

Tobacco smoke in public houses and restaurants comes from the burning tip of a cigarette (or a pipe or cigar), and from the smoke exhaled by the person smoking. Tobacco smoke has the following constituents and associated health risks:

- The smoke contains tiny particles suspended in gases.

- Thousands of chemicals are present of which some (about 40) are carcinogenic.

- Although nicotine is the main reason for addiction to smoking, it is some of these other ingredients of the smoke that can cause ill-health.

- These ingredients can include carbon monoxide, sulphur dioxide and dioxin and heavy metals such as chromium, lead, and cadmium.  All these present a health risk.  The presence of cyanide and sulphur dioxide in tobacco smoke can cause immediate respiratory effects.

- About 12% of tobacco smoke contains tiny particles about one micron in size which can penetrate the thorax.

- The longer people are exposed to tobacco smoke the more chance they have of its adverse effects.  Children can be affected by even short exposures

# POSSIBLE SOLUTIONS TO TOBACCO SMOKE IN ROOMS

## AIR FILTRATIONS SYSTEMS

With air filtration systems:

- The air is pumped through very fine filters to remove these smoke particles (and dust) before its re-circulation.

- The filters do not remove the smallest particles of tobacco smoke, which can settle on the lungs.

- Some of the smoke particles which might be removed are found to settle on other surfaces, and are not removed at all by the air filtration system.  Dust can be activated by other movements in room, and remain in the atmosphere.

- Proper maintenance is required (filter replacement and cleaning) otherwise they can act as a site for bacteria growth, and be ineffective in removal of smoke.

Note: air filtration should not be confused with air conditioning.  Air conditioning does not reduce indoor air pollution.  Its function is to control indoor air temperature, either by heating or cooling fresh and re-circulating air.

## VENTILATION SYSTEMS

With ventilation systems:

- 10 to 20% of fresh air is introduced from outside.  They expel a similar amount of tobacco-smoke from inside the room.  The remaining air containing tobacco-smoke in the room (80 to 90%) is just re-circulated.

- Most of the gases and particles from tobacco smoke, therefore, remain in the room.

- To secure air of minimal risk to health replacement of tobacco-smoke in air at a rate of 50,000 litres/second has been estimated.  This is equivalent to a gale-force wind blowing through the room – which is unacceptable.

- In public houses and restaurants, ventilation systems have to be set up in the smoking areas – to remove the tobacco-smoke, and introduce “clean” air.

- The equipment has to be properly maintained, and otherwise is not effective.

## REFERENCES

Health and Safety Commission.  Proposal for an Approved Code of Practice on Passive Smoking at Work.  Consultative Document 1999.  London.

National Cancer Institute.  Health Effects of Exposure to Environmental Tobacco Smoke.  US Department of Health and Human Services N.I.H.  Publication No. 99-4645, 1999.

# Text boxes

the scottish parliament science information service

The Scottish Parliament Science Information Service is a unique partnership between the Royal Society of Edinburgh, the Royal Society of Chemistry and the Scottish Parliament Information Centre (SPICe).  Its purpose is to ensure that all Members of the Scottish Parliament have access to reliable, rapid and impartial information on science, engineering and technology-related issues in order to help inform parliamentary activities.

The service is provided through a network of 52 Topic Coordinators who are scientists established in their field. It is intended to provide expert information and interpretation to MSPs and their staff to enable them to make their own judgements.

SPICe Science Briefings are compiled for the benefit of Members of the Parliament and their personal staff. Authors may be available to discuss the contents of these papers with MSPs and their staff who should contact Denis Oag on 85369 email denis.oag@scottish.parliament.uk. Members of the public or external organisations may comment on this briefing by emailing us at spice.research@scottish.parliament.uk However, researchers are unable to enter into personal discussion in relation to SPICe Science Briefing Papers.

Every effort is made to ensure that the information contained in SPICe Science briefings is correct at the time of publication. Readers should be aware however that briefings are not necessarily updated or otherwise amended to reflect subsequent changes.

www.scottish.parliament.uk